## Slide 1: Introduction to Computer Science Illuminated
沈映珊
shenys@m.scnu.edu.cn

## Slide 2: The Hardware Layer
4

## Slide 3: The Hardware Layer (Preface)
Chapter 4 Gates门电路 and Circuits电路
  present the most basic elements in a computer.
  explore how computers use electric signals to manage binary values at the lowest level. (p91)

## Slide 4: Contents
4.1 Computers and Electricity
4.2 Gates
4.3 Circuits

## Slide 5: Chapter 4 Gates and Circuits
Mandatory
  1.What’s the gate?
  2.Three kinds of the basic gates (NOT, AND, and OR)
  3.Two categories of circuits
Extended
  1. XOR, NAND and NOR.
  2. The complement of Adder (half/full adder), Memory.
  3. Integrated circuit (IC,集成电路)/Chip芯片
P110
Summary

## Slide 6: Chapter Goals
Compare and contrast a half adder and a full adder
Describe how a multiplexer works
Explain how an S-R latch operates
Describe the characteristics of the four generations of integrated circuits

## Slide 7: 4.1 Computers and Electricity
We have known:
Computers use electric signals to manage binary values at the lowest level.
Electronic gates require a power supply. In general,
  0 for low voltage signal (0-2V).
  1 for high voltage signal (2-5V)
The bit is transmitted as a pulse of high or low voltage.
p92

## Slide 8: 4.2 Gates and Circuit门电路
What is a gate?
  a device that performs a basic operation on electrical signals,
  门是对电信号执行基本运算的设备
  accepting one/more input signals and producing a single output signal.
  A gate uses one or more transistors to establish how the input value map to the output value.(p99)
  门使用晶体管建立输入值和输出值之间的映射
Circuits
  Gates combined to perform more complicated tasks.
p94,p99

## Slide 9: Basic gates and operations
Basic gates
    NOT 非门
    AND 与门
    OR 或门
    XOR 异或门
    NAND 与非门
    NOR 或非门
Boolean Expression
布尔表达式
Logic Diagram 逻辑图
Truth Table 真值表
p94
How do we describe the behavior of gates and circuits?

## Slide 10
Boolean expressions
Uses Boolean algebra, a mathematical notation for expressing two-valued logic
Logic diagrams
A graphical representation of a circuit; each gate has its
own symbol
Truth tables
A table showing all possible input values and the associated
output values

## Slide 11: NOT Gate 非门
A NOT gate accepts one input value and produces one output value.
A NOT gate accepts one input signal (0 or 1) and returns the opposite signal as output
Figure 4.1 Various representations of a NOT gate
A NOT gate is sometimes referred to as an inverter because it inverts the input value.
p94

## Slide 12: AND Gate 与门
An AND gate accepts two input signals.
If the two input values for an AND gate are both 1, the output is 1; otherwise, the output is 0.
Figure 4.2 Various representations of an AND gate
p95

## Slide 13: OR Gate 或门
If the two input values are both 0, the output value is 0; otherwise, the output is 1.
Figure 4.3 Various representations of a OR gate
p96

## Slide 14: XOR Gate 异或门
An XOR gate produces 0 if its two inputs are the same, and 1 otherwise
Figure 4.4 Various representations of an XOR gate
P96，97

## Slide 15: XOR Gate
Note the difference between the XOR gate and the OR gate; they differ only in one input situation
When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0
XOR is called the exclusive OR

## Slide 16: NAND and NOR Gates 与非门或非门
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively.
Figure 4.6 Various representations of a NOR gate
4–15
Figure 4.5 Various representations of a NAND gate
p97

## Slide 17: Review of Gate Processing
A NOT gate inverts its single input
An AND gate produces 1 if both input values are 1
An OR gate produces 0 if both input values are 0
An XOR gate produces 0 if input values are the same
A NAND gate produces 0 if both inputs are 1
A NOR gate produces a 1 if both inputs are 0

## Slide 18: Gates with More Inputs
Gates can be designed to accept three or more input values.
A three-input AND gate, for example, produces an output of 1 only if all input values are 1.
Figure 4.7 Various representations of a three-input AND gate
P98，99

## Slide 19: Constructing Gates
Transistor
A device that acts either as a wire that conducts electricity or as a resistor that blocks the flow of electricity, depending on the voltage level of an input signal
A transistor has no moving parts, yet acts like a switch
It is made of a semiconductor material, which is neither a particularly good conductor of electricity nor a particularly good insulator

## Slide 20: How does a transistor晶体管 work ?
The connections of a transistor in a computer
Figure4.8 The connections of a transistor
源极
基极
发射极
+5V
0V
Two states of a transistor
  ON: 1
  OFF:0
output
p100
开关
Gate: “Switch”
input

## Slide 21: Constructing Gates
Considering the way a transistor works
The easiest gates to create are the NOT, NAND, and NOR gates.
p99

## Slide 22: 4.3 Circuits
What’s a circuit?
  A circuit is a combination of interacting gates designed to accomplish a specific logical function.
  电路是相互关联的门的组合，以用于实现特定的逻辑功能。
p101

## Slide 23: Circuits
Categories
Combinational circuit组合[逻辑]电路
The input values explicitly determine the output
Sequential circuit时序[逻辑]电路
The output is a function of the input values and the existing state of the circuit
We describe the circuit operations using
  Boolean expressions
  Logic diagrams
  Truth tables
Are you surprised?

## Slide 24: Combinational Circuits
Gates are combined into circuits by using the output of one gate as the input for another

## Slide 25: Combinational Circuits
Three inputs require eight rows to describe all possible input combinations
This same circuit using a Boolean expression is (AB + AC)

## Slide 26: Combinational Circuits
Consider the following Boolean expression A(B + C)
Does this truth table look familiar?
Compare it with previous table

## Slide 27: Combinational Circuits
Circuit equivalence
Two circuits that produce the same output for identical input
Boolean algebra allows us to apply provable mathematical principles to help design circuits
A(B + C) = AB + BC (distributive law) so circuits must be equivalent

## Slide 28: Properties of Boolean Algebra

## Slide 29: Adders
At the digital logic level, addition is performed in binary
Addition operations are carried out by special circuits called, appropriately, adders

## Slide 30: Combinational Circuits .vs. Sequential Circuits
Outputs are functions of inputs, output value is determined by input values.
often used to change data.
Outputs are used as inputs. Outputs can be held until inputs change.
often used to store data memory for example.
An S-R latch 触发器 (p108)
A half adder 半加 (p105)

## Slide 31: Adders
The result of adding two binary digits could produce a carry value
Recall that 1 + 1 = 10 in base two
Half adder半加器
A circuit that computes the sum of two bits and produces the correct carry bit
Truth table
p105

## Slide 32: Adders
Circuit diagram representing a half adder
Boolean expressions
sum = A  B
carry = AB

## Slide 33: Adders
Full adder全加器
A circuit that takes the carry-in value into account
Figure 4.10 A full adder

## Slide 34: Multiplexers
Multiplexer
A circuit that uses a few input control signals to determine which of several output data lines is routed to its output

## Slide 35: Multiplexers
The control lines S0, S1, and S2 determine which of eight other input lines
(D0 … D7)
are routed to the output (F)
Figure 4.11 A block diagram of a multiplexer with three select control lines

## Slide 36: Circuits as Memory
Digital circuits can be used to store information
These circuits form a sequential circuit, because the output of the circuit is also used as input to the circuit

## Slide 37: Circuits as Memory
An S-R latch stores a single binary digit (1 or 0)
There are several ways an S-R latch circuit can be designed using various kinds of gates
Figure 4.12 An S-R latch

## Slide 38: Circuits as Memory
The design of this circuit guarantees that the two outputs X and Y are always complements of each other
The value of X at any point in time is considered to be the current state of the circuit
Therefore, if X is 1, the circuit is storing a 1; if X is 0, the circuit is storing a 0
Figure 4.12 An S-R latch

## Slide 39: Work or Rest?

## Slide 40: 4.6 Integrated Circuits 集成电路
p109
Integrated circuit (also called a chip芯片) (p109).
A piece of silicon on which multiple gates have been embedded
Silicon pieces are mounted on a plastic or ceramic package with pins along the edges that can be soldered onto circuit boards or inserted into appropriate sockets

## Slide 41: Integrated Circuits
Integrated circuits (IC) are classified by the number of gates contained in them

## Slide 42: Integrated Circuits
Figure 4.13 An SSI chip contains independent NAND gates

## Slide 43: 4.7 CPU Chips
The most important integrated circuit in any computer is the Central Processing Unit, or CPU.
Each CPU chip has a large number of pins through which essentially all communication in a computer system occurs.

## Slide 44: CPU Chips (Example 1/3)
45nm工艺晶体管芯片（Intel，2007-11-12）
现在45纳米工艺的四核处理器能容纳超过18 亿个晶体管

## Slide 45: CPU Chips (Example 3/3)
铜互连技术（多层）
在CPU核心内电流从铜互连的导线上流过

## Slide 46: Growth of Transistor Counts -Moore’s Law 摩尔定律

## Slide 47: Moore’s Law
Gordon E. Moore in 1965
… the number of circuits that could be placed on a single integrated circuit each year…
Intel
Now?

## Slide 48: What’s Moore’s Law of your own…？

## Slide 49: Chapter 4 Summary
Transistors→Gates→Circuits→Integrated Circuits（ICs）
The flow of electricity is guided by electronic devices called gates, which perform basic logical operations such as NOT, AND, and OR.
Gates can be combined into circuits to perform more complex tasks such as adding, multiplexers, and storing data.

## Slide 50: What’s the point today ?
?
(1) Today ?
(2) Mine ?
(3) Suggestions for Keynote Speakers

## Slide 51: Ethical Issues
Violation of Ethics Codes
Can you give examples of these issues?
Intellectual Property
Quality of Work
Liability for Unreliability
Unauthorized Access
Conflict of Interest

## Slide 52: Who am I?
All the world knows my name. What is
it and why do people know it?

## Slide 53: Do you know?
What is the name of the study of materials
smaller than 100 nanometers?
What did Maurice Wilkes realize in 1949?
What's wrong with uploading your photos
to a social networking site?
What change did Facebook make in 2011?