## Slide 1: Introduction to Computer Science Illuminated
沈映珊
shenys@m.scnu.edu.cn

## Slide 2: The Hardware Layer
4

## Slide 3: Chapter 5 Computing Components
Mandatory
  1.Von Neumann Architecture.
  2.The Fetch-Execute Cycle / Instruction Cycle / Processing Cycle.
  3.ROM and RAM.
Extended
  1. Flash memory.
  2.Secondary memory (Magnetic disk, Touch screens).

## Slide 4: Computer Components
Consider：
If you want to buy a PC or a laptop, What’s your consideration?
Exceptional Performance and Portability
参数如下:
1.Intel Core i7-7700处理器,≥16GB DDR4 2400MHz DIMM;
2.配24寸窄边框液晶显示器,分辨率≥1920*1080,支持HDMI或VGA等接口;
3.NVIDIA GTX1080 8G 256bit GDDR5，单风扇涡轮散热，3年主机厂商上门服务；
4.搭配独显，支持集显+独显端口同步多屏输出；
5.256G PCIE SSD固态，≥1.2GB/秒读写速率；1TB 7200转 3.5寸SATA硬盘，免工具拆装设计;
6.前置接口≥4个USB3.0、≥2个音频端口；
7.后置接口≥2个USB3.0、2个USB2.0，≥1个千兆网RJ45接口，PS/2 端口，1个串口，3音频接口：1个音频输入，1个音频输出，1个麦克风连接口；8.≥400W 80plus 92%金牌认证电源；

## Slide 6: Sizes in Perspective
What is a hertz?

## Slide 7: 5.2 Stored-Program Concept 存储程序
Major Characteristics of Computer Design
  Data and instructions are logically the same and can be stored in the same place.
  The units that process information are separated from the units that store information.
Characters to be remembered:
  John von Neumann
  J.Presper Eckert and John Mauchly
p123

## Slide 8: The von Neumann Machine
John von Neumann and his machine

## Slide 9: 5.2.1 von Neumann Architecture
Five components of the von Neumann Architecture
  The Memory unit 内存 that holds both data and instructions.
  The Arithmetic/Logic Unit 算术逻辑单元格(运算器) that is capable of performing arithmetic and logic operations on data.
  The Input Unit 输入设备 that moves data from outside the computer into the computer.
  The Output Unit 输出设备 that moves results from inside the computer to the outside world.
  The Control Unit 控制器 that acts as the stage manager to ensure that all the other components act in concert.
p123

## Slide 10: The von Neumann architecture
Figure 5.1 The Von Neumann architecture
p125

## Slide 11: The von Neumann architecture (cn)
输入
设备
输出
设备
CPU
控制器
算术逻辑单元格(运算器)
内存
(主存储器)
辅助
存储器
p125

## Slide 12: (1)Memory 内存/主存
Memory is a collection of cells单元.
  each with a unique physical address 物理地址, and
  each store a number of bits.
?physical address
Physical
p123

## Slide 13: The Memory’s Addressability
Addressability 可寻址能力
  The number of bits stored in each addressable location in memory.
  内存中每个可设定地址的位数
Today most computers are byte addressable 字节可编址.
n-bit machine can address 2n different cells. n位处理器可产生2n个不同的地址
p123

## Slide 14: (2) Arithmetic/Logic Unit 算术逻辑部件（运算器）
Arithmetic/Logic Unit (ALU)
  The computer unit that performs arithmetic operations (addition, subtraction, multiplication, and division) and logic operations (NOT,AND, and OR etc.).
The ALU operates on words. ALU操作的是字
  The word length is the size of quantities processed by the ALU.
  计算机的字长是ALU处理的量的大小
p126

## Slide 15: (3) Input/Output Units (I/O设备)
Input Unit 输入设备
  A device that accepts data to be stored in memory.
  Keyboard, mouse, touch screen and scanning device…
Output Unit 输出设备
  A device that prints or otherwise displays data stored in memory or makes a permanent copy of information stored in memory or another device.
  Monitors, Printers…
p127

## Slide 16: (4) Control Unit 控制器
Control Unit
  The computer component that controls the actions of the other components in order to execute instructions in sequence.控制器控制其它部件的动作，以能执行指令序列。
The control unit includes two register 寄存器
  IR指令寄存器：存储当前执行的指令；
  PC程序计数器：存放下一条要执行的指令的地址
CPU = ALU + Control Unit
  Central processing Unit 中央处理器
How does data move?
p127，p128

## Slide 17: How does data move between the different components of a computer?
The parts are connected to one another by a collection of wires called a bus 总线.
Figure 5.2 Data flow through a Von Neumann architecture
Bus
  A set of wires that connected all major sections of a machine through which data flows. 把机器的主要组成部分连接在一起的一组电线，数据在这组电线中流动。
p128

## Slide 18: Motherboard 主板/母板 (1/2)
Motherboard
  The main circuit board of a personal computer.个人计算机的主电路板
The motherboard also has the connections for attaching other device to the bus, such as a mouse, a keyboard, or a hard disk.
p128

## Slide 19: Motherboard 主板/母板 (2/2)

## Slide 20: 5.2.2 The Fetch-Execute Cycle
How does CPU do its job?
CPU interprets and executes instructions by repeating instruction cycle or processing cycle.
The Fetch-Execute Cycle 取-执行周期
  Fetch the next instruction 取指令
  Decode the instruction 译码
  Get data if needed 取数据(如果有需要)
  Execute the instruction 执行指令
The process starts with the address in memory of the first instruction being stored in the program counter (PC,程序计数器)
指令周期
p128
Notes: 先讲cn版本，自己看en版

## Slide 21: The Fetch-Execute Cycle
Figure5.3 The fetch-execute cycle
p130

## Slide 22: CPU 取-执行周期(cn)
CPU对指令的解释和执行是通过重复指令周期进行的。
取-执行周期/指令周期
  取指令；
  译码；
  取数据（如果有需要）；
  执行指令
P128 cn

## Slide 23: 例1：非访问内存的指令执行周期

## Slide 24: 例2：直接访问内存的指令执行周期

## Slide 25: 5.2.3 ROM and RAM
RAM | ROM
Random Access Memory | Read Only Memory
Volatile 易失的 | Non-Volatile
Storing what ? | Storing what ?
Q&A. What does this mean in the first two line? Storing what ?
p130

## Slide 26: Flash Memory (1/2)
Flash memory is a non-volatile computer storage that can be electrically erased and reprogrammed. It is a technology that is primarily used in memory cards and USB flash drives for general storage and transfer of data between computers and other digital products.
It is a specific type of EEPROM (Electrically Erasable Programmable Read-Only Memory电可擦可编程只读存储器) that is erased and programmed in large blocks.

## Slide 27: Flash Memory (2/2)
Example applications include Smart phone, laptop computers, digital cameras and Pad.
It has also gained popularity in the game console market, where it is often used instead of EEPROMs or battery-powered static RAM (SRAM) for game save data.
A USB flash drive

## Slide 28: 5.2.4 Secondary Storage Devices
Two categories of Storage Devices
  [Main] Memory,
  Second/Auxiliary Storage Device
    Magnetic Tape
    Magnetic Disks
    Compact Disks
Storage device is also an input and an output device.
p131

## Slide 29: Magnetic Tape (p131)
The first truly mass auxiliary storage device was the magnetic tape drive.
sequence access 顺序访问 device, opposite to random access 随机访问.
Figure 5.4 A magnetic tape
5-17
p132

## Slide 30: Magnetic Disks
A read/write head travels across a spinning magnetic disk, retrieving or recording data.
Figure 5.5 The organization of a magnetic disk
p132

## Slide 31: CDs and DVDs
CD (Compact disc 高密度光盘) ,CD Drive
  CD-DA
  CD-ROM
  CD-WORM
  CD-RW
DVD (Digital Versatile Disk 数字化视频光盘)
  DVD-ROM/DVD-R
  DVD-RW
Speed Ratings : 24X for example
  X: 150 kilobytes per second (kBps)
p134

## Slide 32: 5.2.5 Touch Screen
The touch screen has two main attributes.
  display like a regular monitor, and
  detect and respond to the user touching the screen with fingers.
Multi-Touch 多点触控
  → The touch screen serves as both input device and output device.
p135

## Slide 33: conclusion
The main points of von Neumann's system structure (von Neumann theory):
  The program itself is treated as data, and the program is stored in the same way as the data processed by the program
  The number of a computer is used binary system
  Computers should be executed sequentially.
冯·诺依曼体系结构(冯·诺依曼理论)要点：
  把程序本身当作数据来对待，程序和该程序处理的数据用同样的方式储存
  计算机的数制采用二进制
  计算机应该按照程序顺序执行

## Slide 34: Synchronous processing
One approach to parallelism is to have multiple processors apply the same program to multiple data sets
Figure 5.8 Processors in a synchronous computing environment
5.4 Parallel Architectures——non von Neumann architecture
p141

## Slide 35: Pipelining
Arranges processors in tandem, where each processor contributes one part to an overall computation
Figure 5.9 Processors in a pipeline

## Slide 36: Shared Memory Parallel Processor
Communicate through shared memory
Figure 5.10 Shared memory configuration of processors

## Slide 37: Limitation of computers with von Neumann Architecture
从本质上讲，冯.诺依曼体系结构的本征属性就是二个一维性，即一维的计算模型和一维的存储模型.
  传统的冯·诺依曼型结构属于控制驱动方式。它是以命令式语言为对象，指令的执行次序受指令计数器的控制，因而指令是串行执行的.
  由于传统冯.诺依曼计算机体系结构天然所具有的局限性，从根本上限制了计算机的发展。
非冯·诺依曼型的程序设计语言:
  探索了适合于除命令式语言的新型计算机系统结构，
  脱离冯·诺依曼原有的计算机模式，开发高度并行功能的新型计算机模型
  例如光子计算机（光处理器利用光的高速和无干扰性，使用光学元件构成处理器。尚在研发中），并行计算机、数据流计算机以及量子计算机等。
External knowledge

## Slide 38: Chapter 5 Summary
This chapter is about the primary components of a computer in the von Neumann architecture.
  Memory Unit, CPU (Arithmetic/Logic unit, Control unit), and I/0 Device.
  These parts are connected to one another by BUS, through which data travels within the computer.
The Fetch-Execution Cycle is the heart of processing.
  Fetch→Decode→[Get data]→Execute

## Slide 39: Who am I?
A lawsuit determined my legacy.
What was it all about?

## Slide 40: Do you know?
Maurice Wilkes discovered what within six
weeks of beginning to program?
Bush received 4,258 votes and Kerry received
260 votes, out of 638 votes cast. ???
Who was the father of the computer?
What did President Obama refuse to give up?

## Slide 41: What’s the point today ?
?
(1) Today ?
(2) Mine ?
(3) Suggestions for Keynote Speakers